Capstone Project Required Revisions

TX System

1. Implement a fixed packet length for the RF system. Modify TX_SYSTEM to only transmit when a specified minimum number of bytes are in the FIFO. Modify FIFO to output number of bytes. Modify TX_SYSTEM to read number of bytes in FIFO and TX when over the minimum required. Recommend a power of 2 where message and CRC fall on 32-bit word boundaries. See item 9 of this list.
2. Remove delay elements. They are only there to remove the algebraic loop error Simulink sees between the FIFO model and the TX_SYSTEM when there is no delay element between them. Adding one had a cascading effect that resulted in many others added.
3. Go through HDL Coder output warnings and make corrections. Effects of these warnings on HDL code and subsequent warnings in ISE is unknown.
4. Replace boolean signals with single bit fixed point. This removes a number of warnings that appear in ModelSim/Questa due to boolean type conversion conflicts in the way HDL Coder generates vhdl that result in numeric_std warnings.
5. Change counter bit widths to the minimum number of bits required to count to the target count value. The counter bit widths are currently excessive and the resulting HDL generates a number of warnings in Xilinx ISE.
6. Change all counters internal structure to match that of Header_Symbol_Counter with the delay on the output and the feedback from the delay. This prevents the output from indexing one count past the intended output which is a possibility in the HDL generated when the counter's delay element is before the switch.
7. Optional – Add enables to all counters and remove subsystem enables. This would be more representative of hand coded HDL.
8. DONE (May 26, 2012 -QPSK_system_v3g) - Replace hand drawn QPSK_SRRC filter with a Simulink model that codes efficiently in HDL (transposed direct form FIR filter). The hand drawn filter generates approximately 400 warnings on its own.
9. Replace byte wide TX data FIFO with a 32-bit wide FIFO. Modify TX_SYSTEM to accept 32-bit input words and supply a byte at a time into TX RF logic.

RX System