## Slide 1
QPSK Tutorial Project
Building a QPSK transceiver using MATLAB HDL Coder and commodity, open-source hardware
Richard Cagley, Ph.D. Toyon Research Corp. (805) 869-1092 rcagley@toyon.com

## Slide 2: Project Goals
There are three keys things that are currently lacking in order to accelerate radio development (and addressing these deficiencies)
  Software tools (MATLAB HDL Coder for HLS)
  Prototyping platform (COTS FPGA board and Toyon FMC-based RF front-end)
  System integration support (example hardware drivers, tutorials, debugging methodologies)
This demonstration/tutorial project is meant to:
  Provide additional “glue” software and examples that take MATLAB code to a complete FPGA-based wireless transceiver
  Allow these radio implementations to be tested and evaluated on an FPGA Mezzanine Card (FMC) based RF transceiver

## Slide 3: Outline
Benefits of MATLAB HDL Coder for wireless transceiver design work
Toyon’s FMC-based, low-cost Chilipepper RF front-end
Low-cost, ZED (Zynq Evaluation & Development) board
QPSK tutorial project
  Overview
  Code entry for Tx/Rx components and simulation
  Hardware deployment and experimentation
  FPGA based microprocessor interfacing
Summary

## Slide 4: Benefits of MATLAB HDL Coder for Wireless Transceiver Development
MATLAB is an excellent HLS language for implementation of advanced signal processing algorithms in FPGAs
  MATLAB is the de-facto standard for initial implementation of advanced signal processing algorithms
  Unparalleled testbench capabilities mean that very complex stimulus can be generated and processed
  The same floating point code and testbench can be used for fixed-point conversion and RTL generation
When algorithm designers have more control of the destiny of their ideas, FPGA designs can be created more efficiently and more of them can get done
  MATLAB addresses challenging language entry issues including complex algorithms that involve:
    Conditional logic
    Mixed logic/BRAM access
    For loops and vector/matrix operations

## Slide 5: Chilipepper – Toyon’s FMC-Based, Open, Low-Cost Transceiver
Several vendors have developed/marketed FPGA Mezzanine Card (FMC) VITA 57 boards for SDR development
Toyon’s is particularly well suited to real-world prototyping that can lead to a practical radio design
Is available at http://www.toyon.com/chilipepper.asp

## Slide 6: Chilipepper – Toyon’s FMC-Based, Open, Low-Cost Transceiver (cont.)
Based on the Lime Microsystems LMS6002 RF-IC transceiver
  Onboard AVR MCU masks complexity during prototyping (instant on capability) while enabling user to customize
  Full FDD/TDD transceiver functionality for experimentation with real-world waveforms, such as 3GPP

## Slide 7: Low-Cost ZED Board
Keeping with the theme of low-cost, easily accessibly, and open platforms, this tutorial project will use the Digilent/Avnet ZED board
One onboard LPC FMC connector will host Toyon’s radio board
External peripherals can be used to provide for some neat uses of the transport stream, e.g., h.264 transmission

## Slide 8: QPSK Tutorial Project Overview
The goal is to provide the user with three MATLAB based elements:
  MATLAB HDL Coder Tx core
  MATLAB HDL Coder Rx core
  Complete MATLAB simulation that pairs the Tx/Rx cores with a channel model
MATLB HDL Coder Tx core
MCU interface/ modulation
SRRC filtering
SRRC filtering
MATLB HDL Coder Rx core
Frequency offset correction
Time offset correction
Demod and MCU interface
Channel and noise model
Noise
Multi-path
FPGA processor

## Slide 9: What does a complete radio look like?
Along with MATLAB HDL Coder cores we also seek to provide an example for how to create a complete, working transceiver using Xilinx EDK and supporting tools

## Slide 10: Initial Experimental Setup

## Slide 11: Data captured with Chipscope/ Soft-touch over the air
Packet transmission is pretty good at this point
  Chilipepper seems stable
  Chilipepper AGC works
In the process of creating a basic MAC layer and serial port demonstration application

## Slide 12: Set of tutorial labs
Seeking to walk through how to create this reference design with the user on their own using MATLAB to HDL workflow. The labs will include:
  Output a tone
  Receive a tone
  Output a QPSK pattern
  Achieve carrier lock on a QPSK pattern
  Determine timing offset on a QPSK pattern
  Receive and decode a transmitted pattern
  Interface a processor with transmitter in order to output a message
  Receive packet

## Slide 13: Summary
Current development tools and techniques are inadequate for developing future waveforms
  The increasing sophistication of algorithms results in mounting difficulty in translating from high-level models to hardware
  As chip vendors provide larger FPGAs and mixed hardware/software system-on-a-chip (SOC) it becomes an insurmountable task for a new waveform to be implemented through “hand-coding” HDL
Work in this tutorial seeks to provide new and experienced users with an example of a complete, working wireless transceiver
  Extensible to the inclusion of future algorithms
  Low cost with nothing “hidden” to the user